## Slide 1: Building Logic Circuits

## Slide 2: Why Do We need to build Logic Circuits?

## Slide 3: Problem: How To Build an Adder?
We have seen the main binary operators.
  NOT
  OR
  AND
  etc.
How do we use these to build a logic circuit that adds binary numbers?
A | B | Carry In | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 4: Karnaugh Map (K-map)
Simplifying Boolean expressions using laws becomes difficult and error-prone with multiple variables.
Karnaugh Maps allow us to simplify expressions visually.
It is best used for problems with 3 or 4 variables.

## Slide 5: Deriving A function from a K-map
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
AB
C

## Slide 6: Deriving A function from a K-map
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
AB
C
Notes: In deriving the equation from the truth table. The values are tabulated as shown in the slide. From the truth table, the value of AB was column while the value of C was for the row. When AB = 0, and C=0, the value of the function is 0. When AB =0 and C = 1, the value of function is 1. When AB = 11 and C = 0, the value of the function was 1. This was replicated for the entire table.
To derive the function from the K-Map, we will group two continuous cells with value 1 as demonstrated in the table.
Note: This grouping can only be done for 1, 2, 4 or 8 cells because they are multiple of 2s.
In this row, C= 0 which means that the inverse is what will be useful. For the two cells, B only has constant value among the two cells. Hence, it is valid. The value of A is changing thereby making the value of 1 not dependent on it. The first operand was derived.
In the second group, C does not have constant value thereby making it irrelevant to the result of the function. Since AB have constant value, it will be the second operand. However, B has a value of 0 which implies that only the inverse will be used. The was derived.
The equation was tested and the result showed the correctness.
In deriving the equation from the truth table. The values are tabulated as shown in the slide. From the truth table, the value of AB was column while the value of C was for the row. When AB = 0, and C=0, the value of the function is 0. When AB =0 and C = 1, the value of function is 1. When AB = 11 and C = 0, the value of the function was 1. This was replicated for the entire table.
To derive the function from the K-Map, we will group two continuous cells with value 1 as demonstrated in the table.
Note: This grouping can only be done for 1, 2, 4 or 8 cells because they are multiple of 2s.
In this row, C= 0 which means that the inverse is what will be useful. For the two cells, B only has constant value among the two cells. Hence, it is valid. The value of A is changing thereby making the value of 1 not dependent on it. The first operand 𝐵𝐶 ̅ was derived.
In the second group, C does not have constant value thereby making it irrelevant to the result of the function. Since AB have constant value, it will be the second operand. However, B has a value of 0 which implies that only the inverse will be used. The 𝐴𝐵 ̅ was derived.
The equation was tested and the result showed the correctness.

## Slide 7: Deriving A function from a K-map
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 | 0 | 1
00 | 0 | 1
01 | 1 | 1
11 | 1 | 0
10 | 0 | 1
A
BC

## Slide 8: Turning the Function into a Circuit Diagram

## Slide 9
Karnaugh maps (K-map) allow us to build and simplify binary functions.
A K-map provides a function using only and and or gates.
We can simply translate the binary function into a circuit diagram.
Original Slides By Pelumi Apantaku.
Updated Slides by Kevin Chalmers.
Video By Kevin Chalmers.
Images courtesy of Wikimedia.