## Slide 1: Logic gates

## Slide 2: NOT GATE
A not gate inverts the value of its input.
  0 becomes 1; 1 becomes 0.
  FALSE becomes TRUE; TRUE becomes FALSE.
  OFF becomes ON; ON becomes OFF.
It is therefore sometimes called an inverter.
The small BUBBLE (or circle) in the output of the gate means the input is being inverted.
Boolean
Symbol
Truth Table
a
b
a | b
1 | 0
0 | 1

## Slide 3: OR GATE
AN OR gate TAKES TWO inputs and produces one output.
  0 and 0 produces 0.
  All other inputs produce 1.
IF any input to an OR gate is 1 (True, on) then the output is also 1 (True, on). Otherwise it is 0 (false, off).
Boolean
Symbol
Truth Table
a | b | c
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0
a
c
b

## Slide 4: AND GATE
AN AND gate TAKES TWO inputs and produces one output.
  1 and 1 produces 1.
  All other inputs produce 0.
IF both inputs are 1 (TRUE, ON) then the output is 1 (TRUE, ON), otherwise it is 0 (FALSE, OFF).
Boolean
Symbol
Truth Table
a | b | c
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0
a
c
b

## Slide 5: XOR GATE
AN XOR gate TAKES TWO inputs and produces one output.
  1 and 1 produces 0.
  0 and 0 produces 0.
  All other inputs produce 1.
XOR means “exclusive OR” – that is an OR gate where only one input can be 1 (TRUE, ON) not both.
Boolean
Symbol
Truth Table
a | b | c
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0
a
c
b

## Slide 6: NOR GATE
A NOR gate TAKES TWO inputs and produces one output.
  0 and 0 produces 1.
  All other inputs produce 0.
NOR means “NOT OR” – that is an inverse of the OR gate.
The small bubble (or circle) in the symbol indicates inversion on OR.
Boolean
Symbol
Truth Table
a | b | c
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
a
c
b

## Slide 7: NAND GATE
A NAND gate TAKES TWO inputs and produces one output.
  1 and 1 produces 0.
  All other inputs produce 1.
NAND means “NOT AND” – that is an inverse of the AND gate.
The small bubble (or circle) in the symbol indicates inversion on AND.
Boolean
Symbol
Truth Table
a | b | c
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 1
a
c
b

## Slide 8
We have examined six logic gate types:
  NOT
  OR
  AND
  XOR
  NOR
  NAND
We use these basic gates to build complex logical functions.
Original Slides By Pelumi Apantaku.
Updated Slides by Kevin Chalmers.
Video By Kevin Chalmers.